## Slide 1: The chemical industry

## Slide 2: Learning outcomes
By the end of this sub unit you should know:
Industrial processes are designed to maximise profit and minimise the impact on the environment.
There are 7 factors that influence the design of an industrial process. Factors influencing process design include: availability, sustainability and cost of feedstock(s); opportunities for recycling; energy requirements; marketability of by-products; product yield.
What environmental issues need to be considered when designing a chemical process. Environmental considerations include: minimising waste; avoiding the use or production of toxic substances; designing products which will biodegrade if appropriate.

## Slide 3
Industrial processes are designed to maximise profit and minimise the impact on the environment. Be able to give descriptions of flow diagrams for an industrial process with a view to recognising the various strategies employed to maximise profitability and to reduce the impact on the environment.
Factors that influence process design include: availability, sustainability and cost of feedstock(s); opportunities for recycling; energy requirements; marketability of by-products; product yield.
Environmental factors influence industrial process design: Environmental considerations include: minimising waste; avoiding the use or production of toxic substances; designing products which will biodegrade if appropriate. (A case study to be familiar with is how concern for the environment shaped the design of an industrial process manufacturing ibuprofen).
Learning outcomes

## Slide 4
The Chemical Industry
Research and development
Production
Process and review
The stages in the manufacture of a new product is as follows
Scaling up
Laboratory
process
Pilot study

## Slide 5
Raw materials
Fossil fuels
Metallic ores
minerals
Air and water
Raw Material: something which is available naturally.

## Slide 6
A feedstock is a reactant that other products are synthesised or extracted from.
A feedstock is made from a raw material
e.g. Naphtha is the feedstock, it is cracked to produce ethene. The raw material is crude oil.

## Slide 7
Principles of design
Industrial processes are designed to maximise profit and minimise the effect on the environment
There are 7 principles of the design process:
Availability of feedstocks
Cost of the feedstock
*Sustainability of the feedstock
Opportunities for recycling
Energy requirements
Marketability of by-products
Product yield (or atom economy)
*Sustainability means that the feedstock is not going to run out and that it can continue to be supplied in the long term with minimum effect on the environment

## Slide 8
Chemical manufacturing can use batch or continuous processes
Batch: raw materials are mixed together and allowed to react. The product is removed.
Continuous: reactants are fed in one end and the products removed in a continuous flow.
Process chosen to maximise economic efficiency.

## Slide 9
Batch versus Continuous
manufacturing in the Chemical Industry
Batch
Continuous
For
OK for up to 100
tonnes per annum
.
More v
ersatile
.
Good for multi
-
step
reactions
.
OK for over 1000 tonnes per
annum
.
Good for fast single step
processes
.
Easy to automate
.
Against
Contamination
of
product is more
likely.
At times, no product
is made.
(Not in use)
Safety
more
of
an
issue
.
Capital cos
t
is high
.
Less flexible
.
Need to run at full capacity
to make a profit.

## Slide 10: Batch – Drug development

## Slide 11: Batch – whisky production

## Slide 12: Continuous - Blast furnace

## Slide 13: Continuous process – Haber process

## Slide 14: Fertiliser Industry
Haber Process
Ammonia is manufactured from N2 and H2. The nitrogen is available from the raw material, air.
The other feedstock for the manufacture of NH3 is hydrogen which is usually produced from steam reforming of methane.
Stage 3
Catalyst
N2(g) +
H2 (g)
alkali
CO2 removed
Natural
gas
Water
Catalyst
CH4 (g)
H2O(g)
heat
Stage 1
AIR
Catalyst
Stage 2
H2
N2
Recycled gases

## Slide 15: Sulphuric Acid Industry
Sulphuric acid is manufactured by the Contact Process.
Sulphur
Air
burner
S
O2(g)
heat
Stage 1
water
Mixture to
dilute the acid
H2SO4
Catalytic
Converter
Cat=V2O5
SO2(g)
SO3(g)
Stage 2
Oxygen
feedstock
absorber
(In 90%
H2SO4)
98% acid
oleum
Waste gases
Stage 3

## Slide 16
Economic Aspects
Operating Conditions; the conditions under which a chemical process operates are chosen to maximise
economic efficiency.
Raising the temperature may increase the rate of a reaction but it will increase energy costs so may not be economic.
Increasing the pressure may make more product but will mean using stronger reaction vessels and more powerful compressors and therefore not economic.

## Slide 17
Manufacturing costs have to take into account
Capital costs
Fixed costs
Variable costs
Cost of building plant
Research and development
Depreciation of plant
Labour
Land purchase
Raw materials and energy
Packaging
Can the by-products be sold?
Cost of waste disposal
Energy bills
Same if 1 tonne or 1000 tonnes
Related to output

## Slide 18
The UK chemical industry is, by and large, capital rather than labour intensive.
Labour intensive is when there is a workforce and therefore wages have to be paid.

## Slide 19
Environmental considerations include:
minimising waste;
avoiding the use or production of toxic substances;
designing products which will biodegrade if appropriate.
Reduce levels of discharge of harmful chemicals.

## Slide 20
Efficient use of energy is significant to cut costs and recycling of feedstocks is often used.
Location of plant is key. Next to the sea if raw materials coming from abroad.
Location of chemical plants are historical and practical. Next to oil refinery for easy access to feedstock
Safety issues are important